## Slide 1: Area-Optimized UAV Swarm Network for Search and Rescue Operations
Laik Ruetten
Paulo Alexandre Regis, David Feil-Seifer, Shamik Sengupta

## Slide 2: Background
Defining the Problem

## Slide 3: Background
Search and Rescue UAVs
Finding victims
Areas dangerous for humans
Still need a human operator
  If we want more drones, do we need more human operators?
  This is a limitation

## Slide 4: Background
Intelligent UAV Swarms
Self organizing
Larger area in less time
  Number of UAVs not limited by human operators available
  Reduces impact of poor battery life
Complex system with many parts

## Slide 5: Background
Challenges
Need to search efficiently
  Cover as much area as quickly as possible
  Battery life
  Emergency situations
Data is useless unless it can be transferred
  Critical for UAV network to remain intact

## Slide 6: Our Solution
We developed a system where each UAV in the swarm:
Spreads out as far as possible
Ensures that it is within range of the mesh network

## Slide 7
Radius of wireless communication

## Slide 8
Optimized coverage

## Slide 9: Previous Work
Left-Hand Search/the Rubber-Band method

## Slide 10: Previous Work
Left-Hand Search/the Rubber-Band method
One robot:
  Driving forward
Other robot:
  Drives closer when signal between gets weak (under a threshold)
RSSI - Received Signal Strength Indicator
“Search and Rescue Operations with Mesh Networked Robots”Tristan Brodeur, Paulo Regis, David Feil-Seifer, and Shamik Sengupta

## Slide 11: Previous Work
Array of UAVs, sorted by RSSI to coordinator

## Slide 12: Previous Work
Array of UAVs, sorted by RSSI to coordinator

## Slide 13: Proposed Work
Mesh Reliance Architecture

## Slide 14: Straight Line Reliance Architecture
Array of UAVS, sorted by RSSI to coordinator

## Slide 15: Mesh Reliance Architecture
Connectivity Matrix of UAVs, randomly assigned, no coordinator

## Slide 16: Mesh Reliance Architecture
Limits with SLRA Possibilities with MRA

## Slide 17: How Mesh Reliance Architecture is Created
Randomly creating a valid connectivity matrix
There must be at least one 1 in every row
There must be at least one 1 in every column
Each element on the row = column diagonal is a 0
Each UAV must be connected to at least one other UAV
All UAVs must be connected in one swarm (not multiple unconnected sub-swarms)
UAVs do not rely on themselves

## Slide 18: Swarm Control Simulation
Tests in an ideal environment

## Slide 19: Swarm Control Simulation
Ideal Environment
n = 2
  The value of n in free space.
TxPower is arbitrarily assumed to be 1
  Exact value not important for initial simulation tests
Magnitude of RSSI;
  Negative or positive sign refers to the direction the signal is traveling

## Slide 20: Swarm Control Simulation
Ideal Environment
Each UAV’s sensors cover the same amount of area
A UAV moves the same distance every time and does move when it tries to move (no wind effects it, etc)
Battery life (time limit) depletes at a constant rate

## Slide 21: Self Organization
Use of Genetic Algorithms to tune simple Neural Networks

## Slide 22: Self Organization
Use of Genetic Algorithms to tune simple Neural Networks

## Slide 23: Self Organization
Input variables:
x_position
y_position
x_direction
y_direction
unsearched_N
unsearched_S
unsearched_E
unsearched_W
signal_strength
Output Variables:
x_direction
y_direction
Use of Genetic Algorithms to tune simple Neural Networks

## Slide 24: Self Organization
Use of Genetic Algorithms to tune simple Neural Networks

## Slide 25: Test 1: Optimize Area-Coverage with one UAV
Generation 1 Generation 22
Generation 92 Generation 343

## Slide 26: Test 2: Optimize Area-Coverage with multiple UAV

## Slide 27: Test 2: Optimize Area-Coverage with multiple UAV
GA and Neural Networks could be methods to optimize the spread of a swarm communication network
Maybe not on board the drones themselves, but done and controlled remotely on a powerful computer

## Slide 28: Test 3: Optimize Spread of UAV Swarm
The lines show which UAVs rely on each other.
Some UAVs still end up close together due to not seeing UAVs that they do not rely on.
Future work will make the UAVs be able to change their reliance structure mid-flight.
Graphical results of simulation of spreading out UAV swarms
(Left: 8 UAV test result; Right: 20 UAV test result)

## Slide 29: Analysis and Conclusions
What worked and what could be improved

## Slide 30: Analysis
The effect of number of UAVs on Performance
Number of UAVs only has a linear relationship with runtime
Number of UAVs does not affect the rate of progress of the algorithm
This was done in simulation on one computer; In future work, will run algorithm on each individual UAV computer in parallel to decrease runtime

## Slide 31: Conclusions
What worked What could be improved
New system for reliance architecture
Optimal spread for UAV swarms
Linear performance
More efficient swarm control techniques
  (improve GAs, or use different method altogether)
Run simulation in parallel on multiple computers
Mesh Reliance Architecture is static
  (should be given ability to be dynamic)
Only a simulation, need to implement real-life system

## Slide 32: Progress and Future Work
Improvements on both MRA and the control of it

## Slide 33: Improved GA Performance
Multi-objective optimization
Better results in same amount of time
Choose to value area-coverage over communication strength, or vice versa
  Signal strength Area coverage

## Slide 34: Dynamic Mesh Reliance Architecture
Changing reliance on-the-fly
10
2

## Slide 35: Dynamic Mesh Reliance Architecture
Changing reliance on-the-fly
10
2

## Slide 36: Dynamic Mesh Reliance Architecture
Changing reliance on-the-fly

## Slide 37: Dynamic Mesh Reliance Architecture
Used to solve this problem

## Slide 38: Support for more UAVs
100 UAV test
Without improvements vs with improvements

## Slide 39
Fill the upper triangle with 1s
For every row,
Pick one 1 to remain a 1 no matter what
The remaining 1s change to 0s with a probability of
1.0/Num_UAVs
Reflect upper triangle over the row = column diagonal to the lower triangle

## Slide 40
Fill the upper triangle with 1s
For every row,
Pick one 1 to remain a 1 no matter what
The remaining 1s change to 0s with a probability of
1.0/Num_UAVs
Reflect upper triangle over the row = column diagonal to the lower triangle

## Slide 41
Fill the upper triangle with 1s
For every row,
Pick one 1 to remain a 1 no matter what
The remaining 1s change to 0s with a probability of
CONNECTIVITY = 1.0 CONNECTIVITY/Num_UAVs
Reflect upper triangle over the row = column diagonal to the lower triangle

## Slide 42
Fill the upper triangle with 1s
For every row,
Pick one 1 to remain a 1 no matter what
The remaining 1s change to 0s with a probability of
CONNECTIVITY = 0.5 CONNECTIVITY/Num_UAVs
Reflect upper triangle over the row = column diagonal to the lower triangle

## Slide 43
Fill the upper triangle with 1s
For every row,
Pick one 1 to remain a 1 no matter what
The remaining 1s change to 0s with a probability of
CONNECTIVITY = 0.1 CONNECTIVITY/Num_UAVs
Reflect upper triangle over the row = column diagonal to the lower triangle

## Slide 44
20 UAVs Connectivity = 1.0
25 UAVs Connectivity = 0.1

## Slide 45: Acknowledgements
This material is based upon work supported by the National Science Foundation under Grant No. IIS-1757929. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.